## Slide 1: Nifty Node Network
Rushad Antia

## Slide 3: “Master Node”
RJ-45
Used for discovery of nodes on the network
Runs server at static ip
  Nodes connect and exchange information (hostname, ip, sensors)
Holds table of connected devices
Ability to reboot, reset, and upload code to nodes
Node requests information about the network
MN responds by sending a list of connected devices to that node
edison01
10.20.0.10
temp
edison02
10.20.0.11
humidity
edison03
10.20.0.12
light
Node Table:
edison01:10.20.0.10:temp
edison02:10.20.0.11:humidity
edison03:10.20.0.12:light

## Slide 4: Slave Node (Provisioning)
Creates object to connect to the Master Node
User inputs list of sensors that the node has
User starts the master node connection

## Slide 5: Slave Node (joining)
Connects to master node
Requests other connected nodes information
Sees which nodes has what it wants
Makes connections to the nodes that have what it wants
Give me connected node info!!
Here you go
Hmm…who has a light sensor?
I do!!!
Me too!!!
Lets get to know each other

## Slide 6: Problems
Node.JS waits for a socket buffer to fill before flushing.
  No manual way to flush a socket buffer
Devices can’t automatically reconnect after they lose connection.
Intel XDK has tons of bugs in it

## Slide 7: For the future
Make a website where you can monitor the nodes
Mobile code for custom actuation
Some way to auto reconnect
Some way to announce a disconnect from the network